## Slide 1: Chapter 4 Timber Design Code
CIVE480 Timber Structures 2019

## Slide 2: 4.1 Design Method

## Slide 3
1) Design goal — SAFE
Timber design code: O86-14 Engineering Design in Wood (CSA 2017)
Load effect ≤ Resistance
Random variables
Random variables
Reliability-based (or probabilistic) design
Limit states design

## Slide 4
2) Limit states design
Strength
limit states
Serviceability limit states
Maximum load-carrying capacity of the structure
Restrict the normal use and occupancy of the structure
(e.g. excessive deflection, vibration…)
Limit states design

## Slide 5
2) Limit states design — performance function
Principles of reliability-based design consider all of the uncertainties involved in the design process.
Performance function: Z (x1,x2,…,xN), (xi: design variable)
By convention: Z = R-S, (R: capacity, S: demand)
The probability of non-performance: P (Z < 0)
The probability of performance: P (Z > 0)
Limit state: Z = 0

## Slide 6
2) Limit states design — probability of failure
Shaded area stands for the probability of failure, where S > R
Probabilistic design
Each variable is a probability distribution (not a single value)

## Slide 7
2) Limit states design — reliability index
Performance function: Z = R-S
: mean of the distribution
: standard deviation
Probability of failure:
where
is the cumulative distribution function of the standard normal distribution
, is the reliability index
Probability density function of f(Z)

## Slide 8
2) Limit states design — reliability index
There is relationship between the reliability index and probability of failure :
larger leads to smaller .
Reliability index | Probability of failure
1.0 | 0.159
2.0 | 0.0228
3.0 | 0.00135
4.0 | 0.0000316
… | …
1.0 | 0.159
2.0 | 0.0228
3.0 | 0.00135
4.0 | 0.0000316
… | …

## Slide 9
2) Limit States Design — Factored load and resistance
Strength
limit states
≤
Specified loads
Load
factor
Specified
resistance
Resistance
factor

## Slide 10
2) Limit states design — load and resistance factors
: Load factor: ≥1
Resistance factor: ≤1
: Specified resistance
: Specified load
The resistance factor can be calibrated to meet target reliability

## Slide 11: 4.2 Load Types

## Slide 12
1) Specified loads
The loads that need to be considered are as follows:
D – Dead load due to weight of building components
E – Load due to earthquake
L – Live load due to use and occupancy
S – Load due to snow (ice and rain)
W – Load due to wind
……
theconstructor.org

## Slide 13
2) Importance factors
Depend on the type of load and the building use and occupancy.
Applied to:
E (earthquake)
S (snow)
W (wind)
roofdoctorutah.com

## Slide 14
2) Importance factors
 | Snow Loads, IS |  | Wind Loads, IW |  | Earthquake Loads, IE | 
Importance category | Limit State |  | Limit State |  | Limit State | 
 | Ultimate | Serviceability | Ultimate | Serviceability | Ultimate | Serviceability
Low | 0.8 | 0.9 | 0.8 | 0.75 | 0.8 | -
Normal | 1.0 | 0.9 | 1.0 | 0.75 | 1.0 | -
High | 1.15 | 0.9 | 1.15 | 0.75 | 1.3 | -
Post-Disaster | 1.25 | 0.9 | 1.25 | 0.75 | 1.5 | -
Depend on the type of load and the building use and occupancy.

## Slide 15
2) Importance factors
Importance categories:
Low — Low hazard to human life in the event of failure
Normal — All buildings except low, high, or post-disaster
High — Buildings likely to be used as post-disaster shelters (e.g. schools and community centres)
Post-disaster — Buildings essential to provide services in a disaster

## Slide 16
3) Load combinations — ultimate limit state
Case | Principal Loads | Companion Loads
1 | 1.4D | 
2 | (1.25D or 0.9D) + 1.5L | 1.0S or 0.4W
3 | (1.25D or 0.9D) + 1.5S | 1.0L or 0.4W
4 | (1.25D or 0.9D) + 1.4W | 0.5L or 0.5S
5 | 1.0D + 1.0E | 0.5L + 0.25S
Most unfavourable effect considering all possible load combinations
(principal loads only and principal loads + companion loads, 4.1.3.2. 3) of NBCC 2015)

## Slide 17
3) Load combinations — serviceability limit states
Case | Principal Loads | Companion Loads
1 | 1.0D | -
2 | 1.0D + 1.0L | 0.5S or 0.4W
3 | 1.0D + 1.0S | 0.5L or 0.4W
4 | 1.0D + 1.0W | 0.5L or 0.5S

## Slide 18
Example 1: Lintel loads
Determine the design loads for the following conditions:
3 meter long lintel supporting roof and one floor of a school
Tributary width of both roof and floor = 3 m
Specified roof dead load = 1 kPa
Specified floor dead load = 1.5 kPa
Minimum specified roof live load = 1.0 kPa
Specified floor live load = 2.4 kPa
1 in 50 year ground snow load, SS = 1.8 kPa
1 in 50 year associated rain load, Sr = 0.2 kPa
Basic snow load factor, Cb = 0.8
Snow load wind exposure factor, Cw = 1.0
Snow load slope factor, Cs = 1.0
Snow load shape factor, Ca = 1.0
Lintel
Floor
Door Frame
Roof not shown in the figure

## Slide 19
Solution part 1: Lintel loads
Ultimate Limit States:
Uniform specified dead load
Uniform specified floor live load
Uniform specified roof live load
Droof = 1 kPa
Dfloor = 1.5 kPa
Lroof = 1.0 kPa
Lfloor = 2.4 kPa
Tributary width = 3 m

## Slide 20
Solution part 1: Lintel loads
Ultimate Limit States:
Specified snow load
(4.1.6 of NBCC 2015)
Uniform specified snow load *
*Roof snow load and roof live load can be considered independently.

## Slide 21
Solution part 1: Lintel loads
Ultimate Limit States:
D:
D+S+L : [Governs]
D+L:

## Slide 22
Solution part 2: Lintel loads
Serviceability Limit State:
Specified snow load
Uniform specified snow load:

## Slide 23
Solution part 2: Lintel loads
Serviceability Limit State:
D:
D+S+L:
D+L: [Governs]
S+L:
L: [Governs]

## Slide 24
Solution part 3: Lintel loads
Use the following loads for design:
Ultimate limit states — 10.5 kN/m for D;
25.85 kN/m for D+S+L or D+L
Serviceability limit states — 7.5 kN/m for D;
17.7 kN/m for D+S+L or D+L;
10.2 kN/m for L or S+L

## Slide 25: 4.3 Design Factors

## Slide 26
1) Load duration factor, KD
Intensity and duration of applied loads influence the strength of wood (similar to fatigue in metals)
Strength losses even under static loading may lead to failure after a given time
Dead load: self weight of roofs, walls and floors
By Rob Munach

## Slide 27
1) Load duration factor, KD
The specified strengths and capacities in CSA O86 are based on the standard-term duration of the specified loads
Load duration | KD | Explanatory notes
Short term | 1.15 | Last no more than 7 days (e.g. wind, earthquake…)
Standard term | 1 | Between short and long term (e.g. snow, occupancy, wheel loads…)
Long term | 0.65 | Subjected to more or less continuous load (e.g. dead loads, fixed machinery…)
(Table 5.3.2.2 of CSA O86)

## Slide 28
For standard-term loads where PL is greater than PS
where:
PL = specified long-term load
PS = specified standard-term load
= S, L, S + 0.5L, or 0.5S + L, determined using importance factor equal to 1.0
1) Load duration factor — Long-term load factor

## Slide 29
2) Service condition factor, KS
Applied when materials are used in service conditions other than dry
Strengths and capacities are multiplied by the service condition factor, KS
Wood dock
Greatnortherndocks.com

## Slide 30
3) Preservation treatment factor KT
Exposed to conditions that cause decay or deterioration, wood should be treated with preservatives
Dip
treated timber
Pressure
treated timber
Preservatives only penetrate the surface of the wood, offering limited protection
Preservatives are forced deep into the wood, offering better protection
gardenfurnitureland.com
Pressure treated timber

## Slide 31
3) Preservation treatment factor KT
Untreated wood should not be in direct contact with masonry, concrete, or soil when moisture transfer can occur
Post mounts
mogams.com
postprotector.com
Post protector

## Slide 32
4) System factor, KH
Accounts for members acting as part of a system, not independently (e.g. repetitive member systems)
Timber floor joist
Floordecorate.com

## Slide 33
5) Size factor, KZ
Strength properties depend on member size and loading conditions, known as “size effect”
A larger volume of member tends to reduce the apparent strength.
swedishwood.com

## Slide 34
6) Serviceability limit states
Elastic deflection (not exceed 1/180 of the span)
Permanent deformation (upper limit of 1/360 of the span due to long term loads if the long term loads excess 50% of the load combinations for serviceability limit states.)
Vibration (carpet, concrete topping)
Moisture content change (design details)

## Slide 35
Shrinkage or swelling of a wood member can be estimated using the following equation:
where:
S = shrinkage or swelling in the dimensions being considered
D = actual dimensions
Mi = the lesser of the initial moisture content or the fibre saturation point (28%)
Mf = the final moisture content
c = shrinkage coefficient
= for lumber (0.002 perpendicular to grain, 0.00005 parallel to the grain)
6) Serviceability limit states — Moisture content

## Slide 36
This lecture is developed based on the Wood Design Manual [1] and CSA O86-2014 [2].
References
[1] Canadian Wood Council (CWC). 2017. Wood design manual. Ottawa, ON, Canada.
[2] Canadian Standards Association (CSA). 2017. Engineering design in wood. CSA O86-14, Toronto, ON, Canada.
[3] National Research Council (NRC). 2015. National building code of Canada 2015. Ottawa, ON, Canada.