## Slide 1
Canadian
Wood
Council
Conseil
canadien
du bois
Prefabrication for Architects
Considerations in Designing Mass Timber Buildings

## Slide 2: Module 1: Introduction and Project Planning for Optimizing Design
Objectives:
Introduce the prefabrication process of mass timber and early design considerations to optimize design.
Introduction to mass timber
Advantages to Prefabrication
Early considerations for optimizing design
Project planning

## Slide 3: Regenerative

## Slide 4: Mass Timber
Engineered products made from dimensional lumber
Laminated together through the elimination process
Forms large structural elements
Lamination occurs through adhesive, nails, screws, or dowels
  Cross Laminated Timber
  Glulam
  Dowel Laminated Timber
  Nail Laminated Timber
  Mass Plywood
Image of a CLT Panel in the fabrication process. Photo by: Veronica Madonna

## Slide 5: Mass Timber Products

## Slide 6: Glulam and Glulam Panels (GLT)
Dimensional Lumber stacked parallel to each other
Long spans and strength
Image of a glulam beam structure and decking. Source: StructureCraft

## Slide 7: Cross Laminated Timber (CLT)
Dimensional lumber stacked crosswise
Strength, dimensional stability and rigidity
The Cube in Hamburg, Germany, is constructed using CLT panels for floor and wall structure. Photo credit IBA Hamburg, Martin Kunze.

## Slide 8: Nail Laminated Timber (NLT)
The interior of 80 Atlantic Avenue in Toronto, Ontario architectural designed by BPN Quadrangle (formerly Quadrangle Architects Ltd.) utilizes a nail-laminated timber floor deck. Photo credit: Doublespace Photography.
NLT consists of dimensional lumber placed on edge with individual pieces mechanically fastened together by nails or screws

## Slide 9: Dowel Laminated Timber (DLT)
Image of the DLT floor structure at 111 East Grand Office. Source: StructureCraft
Like NLT, except it is fastened together using wood dowels rather than metal screws or nails

## Slide 10: Mass Plywood Panels (MPP)
Image of a mass plywood pavilion. Source: Lever Architecture.
Veneer-based engineered panel comprised of multiple veneers pressed and adhered together

## Slide 11: Advantages of Mass Timber
Construction Advantage
Prefabrication on components provide greater precision and quality control.
Reduced on-site construction.
Aesthetic Advantage
Aesthetic and experiential benefits often make mass timber buildings desirable to tenants as well as aiding in biophilic benefits.
Ecological Advantage
Building represent close to 40% of the greenhouse gas emissions.
Wood has the ability to sequester carbon, and is a low embodied carbon building product.
Speed and cost
Human connection
sustainability

## Slide 12: Additional Advantages
Proven Performance and Safe
Light-weight and Low Embodied Carbon Material
Efficient, Cost-Saving Construction
Thermal and Health Benefits

## Slide 13: Social, Economic, Environmental and Cultural Benefits

## Slide 14: Life Cycle Overview of Mass Timber

## Slide 15: Carbon Emissions
Buildings contribute to over 40% of the total green house emissions globally
Annually, embodied carbon is responsible 11% of global GHG emissions and 28% of global building sector emissions.
Source: Architecture 2030

## Slide 16: Embodied vs. Operation Carbon
Embodied carbon will be responsible for almost half of total new construction emissions between now and 2050.
  Unlike operational carbon emissions, which can be reduced over time with building energy efficiency renovations and the use of renewable energy, embodied carbon emissions are locked in place as soon as a building is build. It is critical that we get a handle on embodied carbon now if we hope to phase out fossil fuel emissions by the year 2050.
Source: Architecture 2030

## Slide 17: Activity – Understanding Mass Timber
Name three mass timber products and how they compare.
What are three advantages of mass timber?
Describe the four benefits to utilizing mass timber.
Notes: Refer to lecture notes for analysis results.

## Slide 18: Advantages of Prefabrication

## Slide 19: Mass Timber and Prefabrication
https://www.canadianarchitect.com/home-products-r-hauz-toronto-ontario-and-intelligent-city-vancouver-british-columbia/

## Slide 20: Benefits of Modular Construction
20-50% increase speed of construction
Potential cost savings of 20%
Big changes are required
Modular manufacturers
Developers
Suppliers
Regulations
Design & Engineering
Investments
Source: McKinsey & Company . (2019, June). Modular Construction: From Projects to Products. Retrieved from McKinsey & Company

## Slide 21: Construction Advantage
Construction speed
Potential 25% quicker than traditional material like concrete
90% reduction in truck deliveries
75% fewer works on active deck
Light Weight Structure
Can reduce foundation sizes
Prefabrication = Less Waste
Precision in fabrication process
Greater quality and quality control
Modular Construction
Brock Commons Tall Wood House during construction. Architect: Acton Ostry, Structural Engineer: Fast+Epp. Photo by: KKLaw

## Slide 22
Source: McKinsey & Company . (2019, June). Modular Construction: From Projects to Products. Retrieved from McKinsey & Company
Various Approaches to Prefabrication

## Slide 23: Prefabrication and Potential Scenarios
Source: McKinsey & Company . (2019, June). Modular Construction: From Projects to Products. Retrieved from McKinsey & Company

## Slide 24: 3D Volumetric Prefabrication
Fully Assembled Units
Maximize productivity benefits and efficiencies
However, limitation include transportation
  Typically, 3.5m wide for non-police escort
Compartmentalized plans
  Hotels
  Student Residence
  Affordable Housing
Source: 3D Volumetric Construction of Hotel Jakarta in Amsterdam.
https://www.derix.de/en/referenzen/X-LAM/hoteljakarta

## Slide 25: 2D Panelized
Panels prefabricated off-site and assembled on site
Flat packed for shipping, more economic shipping costs than 3D Volumetric
However, longer times on site than 3D Volumetric
Permits flexibility for open plan design, ie. Offices
Albina Yard in Portland Oregon by LEVER Architecture. Photo by: Jeremy Bittermann

## Slide 26: Early Considerations For Optimizing Design

## Slide 27: Project Planning

## Slide 28: Project Planning and Time Distribution
Figure 9: Compressing the Typical Construction Schedule with Mass Timber. Potential cost savings in comparison to steel and concrete.
(WoodWorks 2019)

## Slide 29: Traditional Project Delivery - Design-bid-build

## Slide 30: Cooperative Planning

## Slide 31: Integrated Design And Project Delivery

## Slide 32
The Integrated Team

## Slide 33: Key Planning Considerations
Integrated design process to ensure careful considerations of building use, site considerations, structure, systems integration and construction sequencing.
Sufficient time must be budgeted in the planning stages.
Enhanced coordination of systems during the design process.
Prefabrication and detail planning are critical to resolve before construction.
Significantly reduce time during the construction stage and heightened overall quality control.

## Slide 34: Manufacturer Input
Capabilities for product and sizes
Optimize size
Reduce waste
Albina Yard in Portland Oregon by LEVER Architecture. Photo by LEVER Architecture.

## Slide 35: Kit of Parts
Brock Commons Tall Wood House. Architects: Acton Ostry Architects, Structural Engineer: Fast + Epp, Photo By: Pollux Chung

## Slide 36: Know Your Product and Supply Chain March 2021

## Slide 37: Activity – Integrated Design Process
Describe the differences between the design-bid-build and the integrated design process (IDP). Provide a diagram of the relationships. Consider:
    What are the key advantages to IDP in mass timber buildings?
    What is the collaboration process critical?
Notes: Refer to lecture notes for analysis results.

## Slide 38: Module 2: Design Considerations for Optimized Design
Objectives:
Understand key design considerations to optimize design for prefabrication of mass timber design.
Structural design considerations
Fire protection design considerations
Acoustic and vibration design considerations
Retrofits and adding storeys to existing building design considerations

## Slide 39: Design Consideration of Mass Timber Design
Mactan Cebu
International Airport Terminal 2,
Cebu City, Philippines.

## Slide 40: Structural Design Considerations

## Slide 41: Selecting a Mass Timber System
Installation of glulam beam during the construction of the First Tech Credit Union headquarters building in Hillsboro, Oregon.
Source: https://www.capitalpress.com
Strength and stability
Load capacity
Program and use
Long term flexibility

## Slide 42: Common Timber Systems
Framed Systems
Panelized Systems
Hybrid Systems

## Slide 43: Structural System and Program Use

## Slide 44: Structural System and Program Use

## Slide 45: Key Considerations
Program Use
Cost
Fire Protection
Vibration and Acoustic Control
Authorities and Code Requirements

## Slide 46: Factors in Selecting a Structural System
Cost
Cost of design
Cost of materials
Cost of transportation
Cost of installation
Cost of protection and maintenance
Schedule
Shop drawings and approvals
Materials acquisition
Construction productivity

## Slide 47: Factors in Selecting a Structural System
Function
Clear span
Program requirements and long-term flexibility
Depth of members and clear height
Location of bearing walls and other supports
Incorporation of mechanical and electrical systems
Thermal insulation
Code Requirements
Fire protection
Sound transmission
Structural capacity
Durability

## Slide 48: Factors in Selecting a Structural System
Aesthetics
  Appearance of material
  Appearance of finished system
  Architectural blend of form and function
Environmental
  Environmental impact of harvesting, mining, quarrying, and manufacture
  Energy required to manufacture, transport, and install materials
  Thermal efficiency of building systems
  Disposal, recycle or reuse at end-of-life cycle

## Slide 49: Framed Structural System

## Slide 51: Ontario Secondary School Teachers’ Federation
Moriyama & Teshima Architects, www.mtarch.com

## Slide 53: 80 Atlantic Avenue – Toronto Ontario
Quadrangle Architects
https://www.archpaper.com/2020/01/80-atlantic-toronto-timber-office-building/

## Slide 55: Brock Commons Tall Wood House
Acton Ostry Architects

## Slide 56: Timber Bay Design Tool – Fast + Epp Concept Lab
https://www.fastepp.com/concept-lab/timber-bay-design-tool/

## Slide 57: Member Calculator Tool – Fast + Epp Concept Lab
https://www.fastepp.com/concept-lab/calculator/

## Slide 58: Activity – Factors in Selecting a Structural System
Name the six factors described in selecting a structural system.
Utilizing the Fast + Epp Concept Lab Timber Bay sizing tool, calculated the size of the structural members of the following structural grid spans.
  8x6m Office Building, 6 stories with a 60 min fire resistance rating.
  Describe the advantages and challenges in design choices available for the scenario.
Notes: Refer to lecture notes for analysis results.

## Slide 59: Hybrid System

## Slide 61: The Arbour at George Brown College
Moriyama & Teshima Architects and Acton Ostry Architects

## Slide 63: 77 Wade Avenue, Toronto Ontario
BNKC Architects

## Slide 64: 80 M Street, Washington D.C.
Figure 44: 80 M Street in Washington D.C. is a vertical expansion of an existing building. Source: Think Wood.

## Slide 65: Panelized System

## Slide 67: The Cube – Hamburg, Germany
The Cube in Hamburg, Germany, is constructed using CLT panels for floor and wall structure.
Photo credit IBA Hamburg, Martin Kunze.

## Slide 68: Case Study: R-Hauz R-Town, Toronto Ontario
Panelized Cross-Laminated Timber (CLT)

## Slide 69: Case Study R-Hauz, R-Town
Developer: R-Hauz
Architect: CMV Architects
Structural Engineer: Moses Engineering
Cross-Laminated Timber Panels
Concept rendering of the front elevation along Queen Street East in Toronto, Ontario. Image Source: www.r-hauz.ca.

## Slide 70: Case Study: R-Hauz, R-Town

## Slide 71: Case Study: YWCA Supportive Housing Kitchener-Waterloo, Ontario
Panelized Cross-Laminated Timber (CLT)

## Slide 72: Case Study: YWCA Supportive Housing
Concept rendering of the proposed exterior of the YWCA Supportive Housing. Image Source: Edge Architects and Element5.
Architect: Edge Architects
Owners: YWKW
Developer: Melloul Blamey Construction
Mass Timber Fabricator: Element5
Cross-Laminated Timber Panels

## Slide 73: Case Study: YWCA Supportive Housing
Concept rendering of the interior of the ground floor amenity space. The structural grid in this location shifts from a panelized system to a post and panel system. Image Source: Edge Architects and Element5.
Diagram of cross-laminated timber panel distribution. Image source: Edge Architects and Element5.

## Slide 74: Case Study: YWCA Supportive Housing
Left: Diagram of Element5’s CLIP system. Right: Building Diagram illustrating the prefabricated mass timber structural system and exterior envelop components. Image Source: Edge Architects and Element5.

## Slide 75: Case Study: YWCA Supportive Housing
Diagram and description of the process and sequencing of construction. Image Source: Edge Architects and Element5.

## Slide 76: Designing for Fire Protection

## Slide 77: Fire Protection – Key Considerations
Low-rise, Mid-rise, High-rise Code Requirements
Passive Fire Protection Strategies
Active Fire Protection Strategies
Fire Protection During Construction

## Slide 78: Passive Fire Protection Strategies
Fire resistant rating of structure in floors
Level of encapsulated material or char consideration
Fire rating of egress routes
Fire separation requirements
Components and systems are intended to contain fire or slow the spread of fires through the use of fire-resistant building elements

## Slide 79
Active Fire Protection Strategies
Detection and response systems
  Fire dampers
  Closure of automatic doors
  Fire sprinklers activated
  Fire suppression system activated

## Slide 80: Fire Protection – Char Theory

## Slide 81: Fire Protection – Encapsulation
Source: Denis Blount, ARUP – “Knock on Wood: Acoustical Design in Mass Timber Structures”.

## Slide 82: Fire Protection Case Study – Brock Commons Tall House Fire Safety During Construction
High-Rise
  Less than four levels of unprotected wood during construction.
  Protection of wood structural elements by installing a layer of Type X gypsum board and concrete topping as structure is built.
  Functional standpipe in concrete cores.
  On-site security and fire watch
Image: Source: Think Wood, https://www.thinkwood.com/projects/brock-commons-tallwood-house
Image: Source: Think Wood, https://www.thinkwood.com/projects/brock-commons-tallwood-house

## Slide 83: Carbon 12 – Portland Oregon
Image Source:
https://www.kaiserpath.com/carbon12
Images: Andrew Pogue, Marcus Kauffman
Fully Exposed Mass Timber
Maximum height: 9 stories; 85 feet
Maximum area: 405,000 SF total building; 45,000 SF average per floor
Fire-rating requirements: 2-hour primary frame; 2-hour floors

## Slide 84: Designing for Acoustics and Vibration

## Slide 85: Acoustics – STC vs IIC
Source: Denis Blount, ARUP – “Knock on Wood: Acoustical Design in Mass Timber Structures”.
Sound Transmission Class (STC) – Airborne
“Through” partitions
Around partitions (flanking)
Through structural coupling
Impact Sound Isolation (IIC) – Impact
Through floor assemblies
Through structural coupling

## Slide 86: Improving Acoustics
Add Mass
Mass provides weight to mitigate transfer of low frequency sounds. For example, impact noise.
Add Noise Barriers
Add Decouplers
Resilient layers to “separate” materials provides decoupling to reduce the transfer of vibration.
Add insulation and other acoustic absorptive material

## Slide 87: Acoustics – Flanking Control
Source: Denis Blount, ARUP – “Knock on Wood: Acoustical Design in Mass Timber Structures”.
Decoupling of floor topping at CLT
Decoupling walls from space below
Acoustic sealant at partition joints

## Slide 88: Acoustic Treatments on CLT Floor Assembly
Source: Denis Blount, ARUP – “Knock on Wood: Acoustical Design in Mass Timber Structures”.
Reference: Canadian CLT Handbook – 19th Edition, FP Innovations
Notes: Review sources and CLT Handbook for reference

## Slide 89: Acoustic Treatments on CLT Wall Assembly
Source: Denis Blount, ARUP – “Knock on Wood: Acoustical Design in Mass Timber Structures”.
Reference: Canadian CLT Handbook – 19th Edition, FP Innovations

## Slide 90: Other Design Considerations
CLT floor slab is lowered into place and fastened to the glulam columns. Photo: KK Law, Courtesy of Naturally: Wood.
Full scale mockups
Fire proofing of connectors
Vibration and Acoustics
Approval Process and AHJ
Insurance Requirements
Temporary fire protection during construction
Onsite Security and Protection
Supply Chain
Notes: To avoid delays on site, may want to consider full scale mock-ups to sort out connection and construction specifics.

## Slide 91: Activity – Understanding Fire Protection and Acoustics
Name the various passive and active strategies involved in designing for fire protection of mass timber buildings.
What are the two main acoustic concerns when it comes to mass timber buildings?
What are the three main ways to improve acoustical performance and what are some of the key considerations of each?
Notes: Refer to lecture notes for analysis results.

## Slide 92: Retrofits and Adding Storeys to Existing Buildings

## Slide 93: Adding Stories to Existing Buildings and Mass Timber
Illustration representing design opportunities with adding storeys to an existing building. Concept rendering by Studio Veronica Madonna Architect.

## Slide 94: Consideration of Mass Timber and Adding Stories

## Slide 95: South Boston Rivet Factory
Adding storeys to South Boston Rivet Factory, by Margulies Perruzzi Architects.

## Slide 96: South Boston Rivet Factory
Source: https://www.enr.com/articles/51022-former-south-boston-rivet-factory-gets-heavy-timber-upgrade

## Slide 97: Resources

## Slide 98: Module 3: Early Construction Consideration
Objectives:
Understand the key early construction consideration involved with prefabrication and mass timber design.
Building Information Modelling (BIM) and Design for Manufacturing and Assembly (DfMA)
System Integration
Envelop and Moisture Consideratioins
XXXX
Assignment: Embodied Carbon Comparison

## Slide 99: Automation and Industrialization of Mass Timber
Image of an automated fabrication process of mass timber, Katerra.
Source: www.kateria.com.

## Slide 100: Benefits of Prefabrication
Less noise, dust and site disruption
Improved health and safety
Continuity of employment
Workforce upskilling
Predictable product performance
Lower product operational costs

## Slide 101
Image of Element5’s new factory in Ontario. Source: Element5

## Slide 102: Building Information Modeling (BIM) Design for Manufacturing and Assembly (DfMA)

## Slide 104: Importance of BIM and DfMA Integration
Integration of BIM amongst the owner, design and construction team.

## Slide 105: Virtual Design and Construction Modelling
Brock Commons Tallwood House utilized various levels of Virtual Design and Construction Modelling throughout the design and construction process. Source: Wood-Works, Brock Commons Tallwood House: Construction Modelling.

## Slide 106: Mass Timber Factory
Layout of the new CLT line for Element5’s new state-of-the-art mass timber facility in St. Thomas, Ontario. Source: www.ledinek.com

## Slide 107: Digital Twin / Virtual Design and Construction Model

## Slide 108: Video – Digital Twin, Virtual Design and Construction Modeling
https://www.youtube.com/watch?v=ATKpFtzCVFU

## Slide 109: Next Generation
Mass Timber research at ETH Zurich.
Robot – dimROB
Source: “Mobile Robotic Fabrication on Construction Sites: DimRob”

## Slide 110: Activity – Benefits of Prefabrication
1. Which of the following is a benefit of wood prefabrication?
    Process efficiency
    b. Controlled environment
    c. Material efficiency
    d. Sustainability
    e. All of the above
2. Name all six identified benefits of prefabrication.
Notes: Refer to lecture notes for analysis results.

## Slide 111: System Integration

## Slide 112: Prefabrication and System Integration
Right: Image by Cadmakers illustrating the level of detail involved in coordinating MEPF systems for fabrication. Left: Image of plumbing shelving and penetrations through CLT slab (Photo source Structurlam).

## Slide 113
Wood Innovation Centre, University of Northern British Columbia
Source: Michael Green Architecture

## Slide 114
80 Atlantic Avenue, Toronto
Source: Quadrangle Architects

## Slide 115: Case Study: Brock Commons Tallwood House
University of British Columbia

## Slide 116
Brock Commons Tallwood House
18 storeys
53 metres high

## Slide 117: Brock Commons Overview – Video 1
https://www.youtube.com/watch?v=G22kYhaT-h4

## Slide 118: Brock Commons

## Slide 119: Virtual Design and Construction Modelling

## Slide 120
Brock Commons

## Slide 121
BROCK COMMONS TALLWOOD HOUSE: CONSTRUCTION OVERVIEW

## Slide 122: Brock Commons Design Process – Video 2
https://www.youtube.com/watch?v=ABQHbNwvU_s

## Slide 123: Brock Commons Project Schedule Overview

## Slide 124: Full-Scale Mock-Up
Brock Commons

## Slide 125: Construction Planning
Photography by KK Law

## Slide 126: Kit of Parts
Brock Commons

## Slide 127: Brock Commons Construction Process – Video 3
https://www.youtube.com/watch?v=Fmuj4XeHsbo

## Slide 128: Activity – Benefits of VDC Modelling
Describe the benefits of VDC modelling. What advantages did it offer on the Brock Common’s Tallwood House and why was it an important aspect of the success of the project?
Notes: Refer to lecture notes for analysis results.

## Slide 129: Envelop & Moisture

## Slide 130: Envelop and Enclosure
The Arbour, Moriyama & Teshima Architects / Acton Ostry Architects
Notes: Moisture control of the mass timber, is critical.
In thinking about construction, the best defence is to close the building up as quickly as possible to prevent moisture saturation and potential staining on the mass timber.
It is ok to get the wood wet, but it is important to allow it to dry out appropiately before any encapsulation occurs.
The mass timber is prefabricated, and will go up quickly. The Arbour utilizes a prefabricated wall system, that will be built off site and be installed in tandum with the mass timber structure.

## Slide 131: Temporary Protective Roofing
Temporary protective roofing at the Limnologen Vaxjio construction site, Sweden.

## Slide 132: Prefabricated Envelopes
Source: Island Exterior

## Slide 133: Managing the Risk of Water Damage During Construction
https://www.surfacesreporter.com/articles/72301/mass-timber-architecture-benefits-and-common-misconceptions

## Slide 134: Managing the Risk of Fire During Construction
Fire protection system
Clean site, reduce flammable
Hot work, such as welding, was done ahead of the mass timber structure installation.
All trades were required to take fire-prevention and fire response training.
Temporary fire doors were installed on the two exit stairs and clear exit paths were maintained.

## Slide 135: Module 4: Life Cycle Assessment
Objectives:
Describe Life Cycle Assessment and the consideration involved in holistic design.
Holistic considerations of carbon
Why is LCA and Carbon Analysis Important
Life Cycle Assessment Tools
Biophilia, Health and Wellness

## Slide 136: Holistic Considerations of Carbon
Looking Towards The Future

## Slide 137: Life Cycle Assessment
Life Cycle Assessment (LCA) is a cradle-to-grave analysis technique to assess environmental impacts associated with all the stages of a product’s life.
The five key stages of LCA include:
Manufacturing
Packaging
Distribution
Use
Disposal
Raw Materials

## Slide 138: The Process of Whole-Building LCA
Source: Athena Sustainable Materials Institute, “About Whole-Building LCA and Embodied Carbon,” 2019.

## Slide 139: Operational Carbon
OPERATIONAL CARBON is defined as the greenhouse gas emissions associated with the operational energy use of a building. This includes all carbon from energy required to heat and power the building, including but not limited to lighting, plug loads, heating and cooling, and cooking.

## Slide 140: Embodied Carbon
EMBODIED CARBON is defined as the greenhouse gas emissions associated with the raw material extraction, manufacturing and processing, transportation, and installation of all building materials.

## Slide 141: Net-Zero Carbon
NET-ZERO CARBON is defined as the combined operational and embodied carbon being resolved as zero through material selection, renewable energy and approved appropriate offsets.

## Slide 142: LCA / LCI / LCIA and LCC
Life Cycle Assessment (LCA)
Calculating the lifetime environmental impact of a product or service.
Life Cycle Inventory (LCI)
Data collection portion of LCA. The accounting of everything involved in the system.
Life Cycle Impact Assessent (LCIA)
What does it mean? The inventory is analyzed for environmental impact.
Life Cycle Costing
Direct monetary cost involved with a product or service on the environmental.

## Slide 143: Life Cycle Assessment

## Slide 144: Whole-Building LCA Explained
LCA looks at cradle-to-grave lifetime of buildings including as resources are consumed and emissions created during each phase of a building’s life span.
  Manufacturing and transportation of construction materials
  Process of construction
  Long phase of building occupancy and maintenance
  Demolition
  Removal of waste materials

## Slide 145: Activity - Life Cycle Assessment
What is the definition of Life Cycle Assessment and what are the five stages of consideration?
What are five phases of a building?
Notes: Refer to lecture notes for analysis results.

## Slide 146: Why is LCA and Carbon Analysis Important?
Working Towards Climate Stability

## Slide 147: 2060 Global Building Stock
Architecture 2030, “Why The Building Sector?,” accessed May 12, 2021, https://architecture2030.org/buildings_problem_why/.
Over the next 35 years,
  2.5 trillion ft2
  of buildings will be constructed or renovated in cities worldwide

## Slide 148: Global CO2 Emissions by Sector
Buildings contribute to over 40% of the total green house emissions globally
Annually, embodied carbon is responsible 11% of global GHG emissions and 28% of global building sector emissions.
Source: Architecture 2030

## Slide 149: Why is Reducing Embodied Carbon Important?

## Slide 150: Embodied vs. Operation Carbon
Embodied carbon will be responsible for
  almost half of total new construction
    emissions between now and 2050.
Source: Architecture 2030

## Slide 151: Canada Raising Climate Ambitions
Federal Government Announcement - April 21, 2021
Go beyond their 30% by 2030
Reduce 2005 emission levels by 40-45% by 2030
Net zero by 2050
Price on pollution
Decarbonizing materials
concrete, steel and aluminum
Will make it law
Notes: One of the drivers that we hear a lot of today is that the impact that mass timber can have on climate stability
As you may know, the federal government recently released announced accelerating environmental targets
- Go beyond 30% carbon reduction by 2030 ….

## Slide 152: Accelerating to Zero by 2040
Source: Architecture 2030
Notes: In addition, world organizations such as Architecture 2030, are adopting similar programs to accelerate carbon positivity – to move 2050 to 2040.
For all new buildings and major renovations – zero-net-carbon (ZNC) operations as soon as possible
For embodied carbon – a 40% reduction as soon as possible for all new buildings, infrastructure, and major renovations, and 65% by 2030.
For existing buildings – a 65% reduction by 2030 in operational carbon emissions.
Zero carbon emissions for the entire built environment by 2040.

## Slide 153: 50% of wood is carbon
Notes: Wood is a renewable and naturally growing material that can sequester carbon from the earth’s atmosphere. The manufacturing of wood products for construction produces low carbon emissions from fossil sources than other building materials, therefore offering a low embodied carbon solution. Prefabricated processes commonly used for products like mass timber create less waste and use less energy than traditional building materials. In addition, the potential available in reducing on-site construction are all factors that benefit the environment.
  Carbon sink: approx. 50% of the weight of wood is solid carbon, absorbed as CO2
  Renewable Resource
  Less waste in construction through prefabrication, lamination of smaller elements in a controlled environment
  Tangible/material commitment to the environment
  only building material grow

## Slide 154: Sustainable Forests Strategy
https://www.ontario.ca/page/sustainable-growth-ontarios-forest-sector-strategy

## Slide 155: Activity – Building and Impact on Climate
Define the following terms:
  Operational Carbon
  Embodied Carbon
  Net-Zero Carbon
Why are each important consideration?
Why is the consideration of embodied carbon critical in achieving climate stability?
Notes: Refer to lecture notes for analysis results.

## Slide 156: Life Cycle Assessment Tools
Gestimat, Athena and Other Tools

## Slide 157: Life Cycle Assessment Workflow
Data Gaps: Some important products and processes are missing or incomplete in the Life Cycle Inventory (LCI) databases. Materials and Energy data is fundamental to whole-building LCA.
Data Inconsistency and Lack of Detail: Currently, there could exist variation in the method and quality of the data. Data on materials may be out of date, and may not adequately resemble regional circumstances.
Method and Standards Inconsistency: There may be variation in approach to LCA, which means results may not be comparable across studies.

## Slide 158: Gestimat
https://gestimat.ca

## Slide 159: Comparative Analysis - Gestimat

## Slide 160: Gestimat – Comparing Results

## Slide 161: Gestimat – Precalculated Typical Buildings

## Slide 162: Tool – Athena Impact Estimator

## Slide 163: Activity - Embodied Carbon Analysis using Gestimat
Using the Gestimat program, perform a carbon comparison analysis of the following building using the following systems:
  Steel
  Hybrid – Steel structure and CLT deck
  Mass timber
Building Specifications:
  Begin with the typical commercial building (start with the predefined building in the system)
  6 stories
  Total Floor Area: 5400 m2
  Building Footprint: 900 m2
  Location: Toronto, Ontario
  Include Foundations:
    15mPA Concrete, 1000m3 Volume
    0.5 metric tons of rebar
Notes: Refer to lecture notes for analysis results.

## Slide 164: Tools